CHONGQING WINYOU POWER CO. LTD

No.13,FENGXI RD., CAIJIAGANG TOWN, BEIBEI DIST., CHONGQING 400707, CHINA

---Specialized in manufacture of Engine, Tiller, Generator and Pump.

CATALOG OF GASOLINE ENGINE

| PHOTO | DESCRIPTION | 40HQ QTY |
| --- | --- | --- |
|  | 152F(97.7cc)/2.5HP Start Mode: recoil start Engine Type: single cylinder, 4-stroke, air-cooled, OHV Max. Power: 1.6kw/3600rpm ; Fuel Tank Capacity: 1.4L; Air Filter: Semi-dry type; Engine Shaft: according to your application | 1554pcs |
|  | 154F(105.3cc)/3HP Start Mode: recoil start Engine Type: single cylinder, 4-stroke, air-cooled, OHV Max. Power: 1.8kw/3600rpm; Fuel Tank Capacity: 1.4L; Air Filter: Semi-dry type; Engine Shaft: according to your application | 1554pcs |
|  | 156F(98.5cc)/3HP Start Mode: recoil start Engine Type: single cylinder, 4-stroke, air-cooled, OHV Max. Power: 4.0kw/3600rpm; Fuel Tank Capacity: 3.6L; Air Filter: Semi-dry type or Oil bath type; Engine Shaft: according to your application | 1460pcs |
|  | 168FA(163cc)/5.5HP(Honda type) Start Mode: recoil start Engine Type: single cylinder, 4-stroke, air-cooled, OHV Max. Power: 4.0kw/3600rpm; Fuel Tank Capacity: 3.6L; Air Filter: Semi-dry type or Oil bath type; Engine Shaft: according to your application | 1460pcs |
|  | 168FB(196cc)/6.5HP(Honda type) Start Mode: recoil start/electric start Engine Type: single cylinder, 4-stroke, air-cooled, OHV Max. Power: 4.8kw/3600rpm; Fuel Tank Capacity: 3.6L; Air Filter: Semi-dry type or Oil bath type; Engine Shaft: according to your application | 1460pcs |
|  | 170F(212cc)/7HP Start Mode: recoil start/electric start Engine Type: single cylinder, 4-stroke, air-cooled, OHV Max. Power: 5.2kw/3600rpm; Fuel Tank Capacity: 3.6L; Air Filter: Semi-dry type or Oil bath type; Engine Shaft: according to your application | 1460pcs |
|  | 173F(242cc)/8HP Start Mode: recoil start/electric start Engine Type: single cylinder, 4-stroke, air-cooled, OHV Max. Power: 5.8kw/3600rpm; Fuel Tank Capacity: 6L; Air Filter: Semi-dry type or Oil bath type; Engine Shaft: according to your application | 620pcs |
|  | 177F(270cc)/9HP(Honda type) Start Mode: recoil start/electric start Engine Type: single cylinder, 4-stroke, air-cooled, OHV Max. Power: 6.6kw/3600rpm; Fuel Tank Capacity: 6L; Air Filter: Semi-dry type or Oil bath type; Engine Shaft: according to your application | 620pcs |
|  | 182F(337cc)/10HP Start Mode: recoil start/electric start Engine Type: single cylinder, 4-stroke, air-cooled, OHV Max. Power: 8.0kw/3600rpm; Fuel Tank Capacity: 6.5L; Air Filter: Semi-dry type or Oil bath type; Engine Shaft: according to your application | 475pcs |
|  | 188F(389cc)/13HP(Honda type) Start Mode: recoil start/electric start Engine Type: single cylinder, 4-stroke, air-cooled, OHV Max. Power: 9.5kw/3600rpm; Fuel Tank Capacity: 6.5L; Air Filter: Semi-dry type or Oil bath type; Engine Shaft: according to your application | 475pcs |
|  | 190F(420cc)/15HP Start Mode: recoil start/electric start Engine Type: single cylinder, 4-stroke, air-cooled, OHV Max. Power: 10.5kw/3600rpm; Fuel Tank Capacity: 6.5L; Air Filter: Semi-dry type or Oil bath type; Engine Shaft: according to your application | 475pcs |
|  | 192F(439cc)/17HP Start Mode: recoil start/electric start Engine Type: single cylinder, 4-stroke, air-cooled, OHV Max. Power: 12.5kw/3600rpm; Fuel Tank Capacity: 6.5L; Air Filter: Semi-dry type or Oil bath type; Engine Shaft: according to your application | 475pcs |
|  | 2v78F(680cc)/22HP Start Mode: recoil start/electric start Engine Type: V-twin cylinder, 4-stroke, air-cooled, OHV Max. Power: 12kw/3600rpm; Air Filter: Semi-dry type; Engine Shaft: according to your application | 271pcs |
|  | 1P65FV(140cc)/5.5HP Min. Oder qty.: a container Start Mode: recoil start Engine Type: Single cylinder, 4-stroke, air-cooled, OHV Max. Power: 3.8kw/3600rpm ; Air Filter: Semi-dry type; Engine Shaft: according to your application | 360/900pcs |
|  | 1P70FV(173cc)/6HP Min. Oder qty.: 100pcs Start Mode: recoil start Engine Type: Single cylinder, 4-stroke, air-cooled, OHV Max. Power: 4.3kw/3600rpm ; Air Filter: Semi-dry type; Engine Shaft: according to your application | 360/900pcs |
|  | 1P70FV-2(196cc)/7HP Min. Oder qty.: 100pcs Start Mode: recoil start Engine Type: Single cylinder, 4-stroke, air-cooled, OHV Max. Power: 5.2kw/3600rpm ; Air Filter: Semi-dry type; Engine Shaft: according to your application | 360/900pcs |
|  | 168F-L(196cc)/6.5HP(with chain reducer) Min. Oder qty.: 100pcs Start Mode: recoil start Engine Type: Single cylinder, 4-stroke, air-cooled, OHV Max. Power: 4.0kw/1800rpm ; Air Filter: Semi-dry type or oil bath type; Engine Shaft: according to your application | 1300pcs |
|  | 177F-L(270cc)/9HP(with chain reducer) Min. Oder qty.: 100pcs Start Mode: recoil start Engine Type: Single cylinder, 4-stroke, air-cooled, OHV Max. Power: 5.7kw/1800rpm ; Air Filter: Semi-dry type or oil bath type; Engine Shaft: according to your application | 620pcs |
|  | 188F-L(389cc)/13HP(with chain reducer) Min. Oder qty.: 100pcs Start Mode: recoil start Engine Type: Single cylinder, 4-stroke, air-cooled, OHV Max. Power: 8.2kw/1800rpm; Air Filter: Semi-dry type or oil bath type; Engine Shaft: according to your application | 620pcs |
|  | 168F-R(163cc)/6.5HP(with clutch reducer) Min. Oder qty.: 100pcs Start Mode: recoil start Engine Type: Single cylinder, 4-stroke, air-cooled, OHV Max. Power: 4.0kw/1800rpm ; Air Filter: Semi-dry type or oil bath type; Engine Shaft: according to your application | 974pcs |
|  | 177F-R(270cc)/9HP(with clutch reducer) Min. Oder qty.: 100pcs Start Mode: recoil start Engine Type: Single cylinder, 4-stroke, air-cooled, OHV Max. Power: 6.6kw/1800rpm ; Air Filter: Semi-dry type or oil bath type; Engine Shaft: according to your application | 480pcs |
|  | 188F-R(389cc)/13HP(with clutch reducer) Min. Oder qty.: 100pcs Start Mode: recoil start Engine Type: Single cylinder, 4-stroke, air-cooled, OHV Max. Power: 8.2kw/1800rpm; Air Filter: Semi-dry type or oil bath type; Engine Shaft: according to your application | 480pcs |

Song Cong

Tel: +86-1770 835 7941

Email: winyou_sc@163.com

Chongqing Winyou Power Co.,Ltd