CHONGQING WINYOU POWER CO. LTD

No.13,FENGXI RD., CAIJIAGANG TOWN, BEIBEI DIST., CHONGQING 400707, CHINA

---Specialized in manufacture of Engine, Tiller, Generator and Pump.

OFFER FOR TILLER ACCESSORIES

| PHOTO | DESCRIPTION | REF. NO. | APPLICATION |
| --- | --- | --- | --- |
|  | φ23 Interlaced paddy wheel One side length: 400mm; match up with crawl plate could be better; Rotating diameter: φ=380mm; Tilling depth：150mm—300mm； Tilling width：850mm； Suitable tiller: all tiller with axle diameter φ23 Function：low-load for machine, easy turnaround | #1 | For shallow paddy fields or slightly hard winter paddy fields |
|  | Efficient paddy wheel One side length: 600mm; match up with crawl plate could be better; Rotating diameter: φ=390mm; Tilling depth：150mm—300mm； Tilling width：1350mm； Suitable tiller: tiller with 178F/186F diesel engine Function：anti-winding and hilling | #2 | For shallow paddy fields or slightly hard winter paddy fields |
|  | Efficient paddy wheel（Little angel type） One side length: 290mm; match up with crawl plate could be better; Rotating diameter: φ=330mm; Tilling depth：290mm； Tilling width：640mm； Suitable tiller: tiller with 178F/186F diesel engine Function：anti-winding and hilling | #3 | For shallow paddy fields or slightly hard winter paddy fields |
|  | Demountable paddy wheel One side length: 600mm; match up with crawl plate could be better; Rotating diameter: φ=390mm; Tilling depth：150~300mm； Tilling width：1350mm； Suitable tiller: tiller with 178F/186F diesel engine; Function：anti-winding and hilling, demountable type for going through the narrow places; | #4 | For shallow paddy fields or slightly hard winter paddy fields |
|  | Crawl plate One side length: 250mm; Rotating diameter: φ=450mm; Suitable tiller: all tiller; Function： when working in very soft paddy field, equip tiller with the paddy wheel or complex paddy blade and crawl on both sides to increase the crawling ability to prevent the tiller being caught in the field. | #5 | For very soft paddy fields |
|  | Crawl plate(five feet type) One side length: 250mm; Rotating diameter: φ=450mm; Suitable tiller: all tiller; Function： when working in very soft paddy field, equip tiller with the paddy wheel or complex paddy blade and crawl on both sides to increase the crawling ability to prevent the tiller being caught in the field. | #6 | For very soft paddy fields |
|  | Stiffened crawl plate One side length: 250mm; Rotating diameter: φ=450mm; Suitable tiller: all tiller; Function： when working in very soft paddy field, equip tiller with the paddy wheel or complex paddy blade and crawl on both sides to increase the crawling ability to prevent the tiller being caught in the field. | #7 | For very soft paddy fields |
|  | Complex paddy blade One side length: 450mm; Rotating diameter: φ=400mm; Tilling depth：300mm； Tilling scope：950mm； Suitable tiller: all tiller; Function： anti-winding, remove the guard plate can be turned into dry-land blade; | #8 | For hard paddy field, shallow paddy field or blister paddy field; land filed |
|  | Iron wheel Outer diameter: 530mm/480mm; Suitable tiller: all tiller; Function: replace rubber wheel for walking in paddy field, such as tiller match with blade plough in rear part then equip the tiller with iron wheel, machine can be flexible to walk in the paddy field; | #9 | For all paddy field |
|  | Anti-skidding iron wheel Outer diameter: 400mm; Suitable tiller: all tiller; Function: replace rubber wheel for walking in paddy field, such as tiller match with blade plough in rear part then equip the tiller with iron wheel, machine can be flexible to walk in the paddy field; | #10 | For all paddy field |
|  | Anti-skidding iron wheel Outer diameter: 300mm; Tilling width: 230mm Suitable tiller: all tiller; Function: welding blade plates are broadening, replace rubber wheel for walking in paddy field, such as tiller match with shovel plow in rear part then equip the tiller with iron wheel, machine can be flexible to walk in the paddy field; | #11 | For all paddy field |
|  | Anti-winding blade One side length: 450mm; Rotating diameter: φ=400mm; Tilling depth：300mm； Tilling width：950mm； Suitable tiller: all tiller; Function： anti-winding, big load,; but not suit for dry cropland | #12 | For harder rice fields and shallow paddy fields with weeds and wasteland |
|  | Hexagon roller blade Rotating diameter: φ=360mm; Tilling depth：250mm； Tilling width：1000mm； Suitable tiller:tiller with 178F/186F diesel engine Function: anti-winding, more efficient working performance; | #13 | For hard paddy field, shallow paddy field or blister paddy field |
|  | Deep tilling blade(Little angel type) One side length: 350mm; Rotating diameter: φ=360mm; Tilling depth：330mm； Tilling width：700mm； Suitable tiller: all tiller; Feature：blade is detached, special for hard land. | #14 | For pretty hard land and paddy field; not suitable for land with full of weeds. |
|  | Simple opener Ditching width：350mm； Ditching depth：300mm； Suitable tiller: all tiller; match with tilling blade , iron wheel Function： ditching and simply ridge | For all land |
|  | adjustable opener adjustable width: 230mm-310mm-390mm-490mm; Height of the blade: 235mm; Height of the opener: 460mm; Suitable tiller: all tiller; match with tilling blade Function： ditching as your demand width; | For all land |
|  | Deflecting shovel plow Max. width: 280mm (adjustable); Total height : 550mm (adjustable); Total length: 630mm (adjustable); Height of triangular spade: 170mm Suitable tiller: tiller with 178F/186F diesel engine Function：ditching with your demand width; Advantage: adopt 65Mn steel plate as raw material, non-fading, durable and indeformable; | For all land |
|  | adjustable opener(with rear wheel) adjustable width: 230mm-310mm-390mm-490mm; Height of the blade: 235mm; Height of the opener: 460mm; Suitable tiller: all tiller; match with tilling blade Function： ditching as your demand width; increase the stability of the ditch operation and effectively reducing the load on the tiller | For all land |
|  | Earth ploughing system (fan type tilling blades+adjustable ditching plow) Opener adjustable tilling width: 290mm~500mm Opener max. tilling depth: 255mm (adjustable); Fan tilling blade rotating diameter: φ=350mm Suitable tiller: all tiller; match with tilling blade Function：high efficient ditching working performance, the ditching inclination and width is adjustable, the bottom spade shape designing makes the land be more smooth. | For all land |
|  | Double head ditching plow Ditching width: 600mm Spacing distance: 300mm; Suitable tiller: all tiller; match with tilling blade and iron wheel; Function： ditching. | For all land |
|  | Three head ditching plow Ditching width: 750mm Spacing distance: 250mm; Suitable tiller: all tiller; match with tilling blade and iron wheel; Function： ditching. | For all land |
|  | Four head ditching plow Ditching width: 600mm Spacing distance: 300mm; Suitable tiller: all tiller; match with tilling blade and iron wheel; Function： ditching. | For all land |
|  | Deep tilling blade One side length: 450mm; Rotating diameter: φ=400mm; Tilling depth：350mm； Tilling width：950mm； Suitable tiller: all tiller; Feature：blade is detached, special for hard land. | For pretty hard land ; not suitable for land with full of weeds. |
|  | Tilling blade One side length: 450mm~600mm; Rotating diameter: φ=400mm; Tilling depth：300mm； Tilling width：900mm~1200mm； Suitable tiller: all tiller; Feature：blade is detached for most kinds of land; | For dry land, hard land, sand land, wasteland, greenhouse, garden, tea garden, tobacco field and so on. |
|  | light-duty shovel plow Max. Tilling depth: 280mm; Max. Tilling width : 410mm (adjustable); Suitable tiller: all tiller; Function：ditching; Advantage: shovel plow tip adopt 65Mn steel plate as raw material, durable and indeformable, sloping angle is adjustable; | For land and terraced field |
|  | light-duty shovel plow Max. Tilling depth: 240mm; Max. Tilling width : 200mm (adjustable); Suitable tiller: all tiller; Function：ditching; Advantage: shovel plow tip adopt 65Mn steel plate as raw material, durable and indeformable, sloping angle is adjustable; | For land and terraced field |
|  | Half-edge ditching plow Max. width: 240mm; Total height : 200mm; Triangular spade thickness: 7mm; Suitable tiller: tiller with 178F/186F diesel engine; Function：ditching; | For all land |
|  | Weeding wheel One side length: 370mm; Rotating diameter: φ=270mm; Suitable tiller: all tiller; Function: weeding, anti-winding, cut off the grass or uproot the weeds; | For all land |
|  | Weeding wheel One side length: 300mm; Rotating diameter: φ=360mm; Suitable tiller: all tiller; Function: weeding, anti-winding, cut off the grass or uproot the weeds; | For all land |
|  | Pentagonal weeding wheel One side length: 325mm; Rotating diameter: φ=230mm; Suitable tiller: all tiller; Function: weeding, anti-winding, cut off the grass or uproot the weeds; | For all land |
|  | Potato plow(integral type) Total height: 460mm; Total length: 590mm; Filter width: 360mm; Suitable tiller: all tiller; Function: harvest potato. | For all land |
|  | Potato plow(split type) Total height: 460mm; Total length: 590mm; Filter width: 360mm Suitable tiller: all tiller; Function: harvest potato. | For all land |
|  | Side disc Outer diameter: 245mm; Function: prevent tilling blades or some other tools being winded by weeds. And help tilling blades to cut off the weeds at the edge. | For all land |
|  | Rotating round pit wheel Outer diameter: 400mm; Function: with the rotation of the wheel, ditch many round pit for seed, and the distance between two pits is same, which is obtained by several experiments. | For all land |
|  | Ridge plow system (Hesheng type) (spiral blades+adjusted ditching plow+flat plate) (Sawtooth spiral tilling blades+ adjusted opener) One side length: 350mm; Rotating diameter: φ=400mm; Tilling depth：200mm~300mm； Tilling width：adjustable； Suitable tiller: tiller with 178F/186F diesel engine; Feature：ridging, ditching, hilling; | For dry land, sand land, not suitable for land with to much weeds. |
|  | Ridge plow system (Jiamu type) (Sawtooth spiral tilling blades+ adjusted shield shape opener) One side length: 350mm; Rotate outer diameter: φ=400mm; Tilling depth：200mm~300mm； Tilling width：adjustable； Suitable tiller: tiller with 178F/186F diesel engine; Feature：ridging, ditching, hilling; | For dry land, sand land, not suitable for land with to much weeds. |
|  | Ridge plow system (Ridge inside type) (hilling blades+ iron wheel+ box ridge former) Ridge height: 360mm; Ridge width: 820mm~360mm(adjustable); Hilling blade one side length：340mm； Rotating diameter：325mm； Suitable tiller: tiller with air cooled diesel engine and gasoline engine; Feature：ridging, ditching, hilling; | For dry land, sand land, not suitable for land with to much weeds. |
|  | Ridge plow system (for diesel tiller) (hilling blades+ iron wheel+box ridge former) Ridge height: 280mm; Ridge width: 820mm~360mm(adjustable); Hilling blade one side length：340mm； Rotating diameter：325mm； Suitable tiller: tiller with 178F/186F diesel engine; Feature：ridging, ditching, hilling; | For dry land, sand land, not suitable for land with to much weeds. |
|  | Ridge plow system (for gasoline tiller) (hilling blades+iron wheel+box ridge former) Ridge height: 280mm; Ridge width: 820mm~360mm(adjustable); Hilling blade one side length：340mm； Rotating diameter：325mm； Suitable tiller: tiller with air cooled gasoline engine; Feature：ridging, ditching, hilling; | For dry land, sand land, not suitable for land with to much weeds. |
|  | Ridge plow system (with flat plate) (hilling blades+box ridge former+flat plate) Ridge height: 360mm; Ridge width: 820mm~360mm(adjustable); Hilling blade one side length：340mm； Rotating diameter：325mm； Suitable tiller: all tiller; Feature：ridging, ditching, hilling; rear flat plate makes the raised row/mounds surface be flat. | For dry land, sand land, not suitable for land with to much weeds. |
|  | Ridge plow system (cutting&split type) (hilling blades+ box ridge former+flat plate) Tilling depth: 200mm~300mm(adjustable); Tilling width: adjustable; Hilling blade one side length：350mm； Rotating diameter：φ=400mm； Suitable tiller: tiller with 178F/186F diesel engine; Feature：ridging, ditching, hilling; The outer spiral blade is detachable, change the tilling width and decrease machine load, after removing a set of black spiral blade, one side tilling width become 260mm; | For all land |
|  | Smoothing harrow(five teeth) Total length: 1030mm; Width: 140mm; Suitable tiller: all tiller; Feature：smoothing land and collect weeds. | For all land |
|  | Ridge plow system (hilling blades+ iron wheel+circular arc ridge former) Ridge former Height: 210mm or 240mm; Ridge former width: φ32-485mm~1200mm /φ23-455mm~880mm; Hilling blade one side length: 340mm; Rotating diameter: 325mm; Suitable tiller: all tiller; Feature：mounds will be ridged in circular arc shape. | For dry land, sand land, not suitable for land with to much weeds. |
|  | Ridge plow system(with skidproof iron wheel ) (Spiral blades + non-skid iron wheel+ ridge former) Ridge former Height: 210mm or 240mm; Ridge former width: φ32-485mm~1200mm /φ23-455mm~880mm; Hilling blade one side length: 320mm; Rotating diameter: 350mm; Suitable tiller: all tiller; Feature： The spiral blades are a lengthened double-decked and crossed structure , more densely pushed and flipped soil, and can be used effectively with tilling and ridging. With skidproof wheel to increase the forward power and support the machine will not sink. Also the rear circular arc ridge former makes mounds be ridged in standard circular arc shape. | For dry land, sand land, not suitable for land with to much weeds. |